## Slide 1: GPU Programming (in CUDA)
Julian Gutierrez
Fall 2018
Session 2

## Slide 2: Outline
CUDA Basics
CUDA Execution Model
Profiling Tools

## Slide 3: CUDA Basics

## Slide 4: CUDA Basics
The language that started the GPGPU excitement
CUDA only runs on NVIDIA GPUs*
Highest performance programming framework for NVIDIA GPUs
Learning curve similar to threaded C programming
  Large performance gains require mapping program to specific underlying architecture

## Slide 5: CUDA Basics
CUDA is a general purpose parallel platform
CUDA is a standard ANSI C-like language
CUDAs Application Programming Interface (API) manages:
  Devices
  Memory
  Synchronization
  Etc.

## Slide 6: CUDA Basics
CUDAs API offers two levels:
  CUDA Driver API.
    Low level API, offers better control over the GPU.
  CUDA Runtime API.
    Higher level; implemented on top of the driver API.
    We will use this API.

## Slide 7: CUDA Basics
C Code
CUDA Code
Threads

## Slide 8: CUDA Basics
Host
  CPU
  Executes the main function and any other CPU related jobs
Device
  GPU
  Executes the kernel functions
CUDA Kernels: data-parallel function
  A kernel is a function callable from the host and executed on the CUDA device.
  The sequential code executed by each thread.
  It runs “simultaneously” by many threads in parallel.
CUDA compiler: nvcc
  Separates the device code from the host code during compilation process.
Concepts

## Slide 9: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
  Copy data back from GPU to CPU (cudaMemcpyDeviceToHost)
Concepts

## Slide 10: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
  Copy data back from GPU to CPU (cudaMemcpyDeviceToHost)
Concepts

## Slide 11: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
    Allocate space
    Transfer data
Concepts
cudaError_t cudaMalloc ( void** devPtr, size_t size )
cudaError_t cudaMemcpy ( void* dst, const void* src, size_t count, cudaMemcpyKind kind )

## Slide 12: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
  Copy data back from GPU to CPU (cudaMemcpyDeviceToHost)
Concepts

## Slide 13: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
    Think about adding 2 vectors with a size of 1000 together:
    Ai + Bi = Ci
    How many threads would you ideally use?
    How do you divide the number of threads?
    What changes if you have a 2D array instead?
    What changes if the solution requires synchronization between certain threads?
Concepts

## Slide 14: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
    Thread organization
      A Kernel call creates a Grid.
      Multiple blocks are combined to form a grid. All the blocks in the same grid contain the same number of threads.
      The threads of a block can be indexed using 1 Dimension (x), 2 Dimensions (x,y) or 3 Dimensions indexes (x,y,z)
      Blocks Per Grid (Grid size)
        blockIdx.x, blockIdx.y, blockIdx.z
        gridDim.x, gridDim.y, gridDim.z (measured in blocks)
      Threads Per Block (Block size)
        threadIdx.x, threadIdx.y, threadIdx.z
        blockDim.x, blockDim.y, blockDim.z (measured in threads)
Concepts

## Slide 15: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
    How do we define the number of blocks per grid, and threads per block?
      Consider the nature of the problem
      Consider the nature of the GPU architecture
      Use dim3 data type
Concepts
dim3 block(32); dim3 grid(((nElem-1)/block.x)+1);
Grid Size is a rounded up multiple of blocks, based on the parallel architecture of the GPU

## Slide 16: CUDA Basics
Flow of a CUDA program
  Copy data from CPU to GPU (cudaMemcpyHostToDevice)
  Invoke Kernels to operate over the GPU data (asynchronous call)
    Invocation of the CUDA kernel from host will have triple-angle-brackets:
    grid*block is the total number of threads launched for the kernel.
Concepts
kernel_name <<<grid, block>>>(argument list);

## Slide 17: CUDA Basics
Kernel Invocation example
  How many threads are executed?
  How do we tell each thread to process one unique element?
Concepts
kernel_name<<<4096, 256>>>(argument list);

## Slide 18: CUDA Basics
Kernel Invocation example
  How many threads are executed?
  How do we tell each thread to process one unique element?
Concepts
kernel_name<<<4096, 256>>>(argument list);

## Slide 19: CUDA Basics
Writing kernels:
  Global qualifier (Executed on the device, Callable from the host only)
  Device qualifier (Executed on the device Callable from the device only)
  Some restrictions:
    Use only device memory (pointers to GPU RAM)
    return void
    no support for variable number of parameters
    It has asynchronous behavior
Concepts
__global__ void kernel_name(argument list);
__device__ called from the device.

## Slide 20: CUDA Basics
Example

## Slide 21: CUDA Basics
Example
Allocation on the GPU
Transfer Data CPU to GPU
Kernel Call
Transfer back to CPU

## Slide 22: CUDA Basics
Example

## Slide 23: CUDA Basics
Compilation
nvcc matrixMul.cu -o matrixMul
Execution
./matrixMul
Sequential Job Time: 588.227987 ms
Parallel Job Time: 108.647108 ms
Example

## Slide 24: CUDA Execution Model

## Slide 25: CUDA Execution Model
Why Do we need to learn about the GPU architecture and the CUDA execution model?
  To understand how to efficiently use the selected configuration
  Find a guideline to choose a proper grid/block configuration
We will go over the architecture while explaining how a kernel executes on the GPU
We will focus on the Kepler architecture
Example

## Slide 26: CUDA Execution Model
The Kepler Architecture
  Divided into SMXs
  Contains a big L2 cache shared between all SMXs
Kepler Architecture - SMX

## Slide 27: CUDA Execution Model
Scalable array of Streaming Multiprocessors
  CUDA Cores
  Shared Memory
  Register File
  Load/Store Units
  Special Function Units
  Warp Scheduler
Streaming Multiprocessor Extreme (SMX)
  Each SM is designed to support the execution of hundreds of threads.
  Kepler K40
    15 Multiprocessors
    Number of processors: 2880
    Each SMX contains
      192 CUDA cores
      64 Double Precision units
      32 SFU
      32 load/store units
Kepler Architecture - SMX

## Slide 28: CUDA Execution Model
Kepler General Information
Details | Kepler GK110
Compute Capability | 3.5
Threads / Warp | 32
Max Warps / Multiprocessor | 64
Max Threads / Multiprocessor | 2048
Max Thread Blocks / Multiprocessor | 16
32-bit Registers / Multiprocessor | 65536
Max Registers / Thread | 255
Max Threads / Thread Block | 1024
Shared Memory Size Configurations (bytes) | 16K 32K 48K

## Slide 29: CUDA Execution Model
When a kernel Grid is launched:
  Thread-blocks are divided among the SMs for execution.
  Threads on the same blocks will be executed simultaneously (logically speaking).
  Multiple blocks could be assigned to the same SM but that doesn't mean they will be executed simultaneously, it will depend on the available resources.
Launching a Kernel

## Slide 30: CUDA Execution Model
Logical and Physical View

## Slide 31: CUDA Execution Model
Launching a Kernel
kernel<<<4, 256>>>(pointer1);
256 threads
256 threads
256 threads
256 threads

## Slide 32: CUDA Execution Model
CUDA uses Single Instruction Multiple Thread (SIMT)
  Threads will be grouped into warps (32 threads per warp)
  All threads in a warp execute the same instruction at the same time
Each SM will partition the blocks into warps and then schedule them for execution depending on available hardware resources.
It is possible that threads on the same warp could have different behavior.
Kepler Architecture - SMX

## Slide 33: CUDA Execution Model
Warp  the basic unit of execution
Each thread in a warp must executed the same instruction.
Warp Execution

## Slide 34: CUDA Execution Model
Blocks can be 3D (x, y, and z dimension). However from the hardware point of view, we can see the threads as one dimension.
Threads are grouped into warps based on the built-in variable threadIdx
  E.g. blocks of 128 threads will be partition in 4 warps as follow:
Warp Execution

## Slide 35: CUDA Execution Model
Not taking warp size into account can lead to misuse
If your block has a certain number of threads which is not a multiple of the warp size, then threads on a warp will be wasted.
    E. g. a threadBlock of 80 threads.
Warp Execution

## Slide 36: CUDA Execution Model
Warps
kernel<<<4, 256>>>(pointer1);
256 threads
256 threads
256 threads
256 threads
warp
warp
warp
warp
warp
warp
warp
warp

## Slide 37: CUDA Execution Model
4 warp schedulers
  Enabling 4 warps to be issued and execute at the same time
  two independent instructions per warp can be dispatched each cycle.
Each SM can issue a maximum of 64 warps (e.g. a total threads = 64 * 32 = 2048 threads resident in the SM)
Warps

## Slide 38: CUDA Execution Model
Active block: when resources such as registers and shared memory have been allocated to it.
Active warp: warps that belong to the active blocks
  Selected warp. Warp that is actively executing
  Eligible warp. Warp that is ready for execution but is not currently executing.
  Stalled warp. Warp that is not ready for execution.
Warps

## Slide 39: CUDA Execution Model
Number of active warps will be limited by physical resources.
if a warp is idle for any reason, SM is free to schedule another warp (from any thread-block that exist already on the SM).
Warps

## Slide 40: CUDA Execution Model
All threads on a warp MUST execute the same instruction.
What happen when there is a branch behavior?
Warp Divergence
CPU
It has complex hardware to specifically handle branch prediction
GPU
No complex branch prediction. Stalling of threads in a warp

## Slide 41: CUDA Execution Model
Avoid branch divergence!
Stalling threads is never a good thing
Only threads on the same warp can decrease performance by divergence
Warp Divergence

## Slide 42: CUDA Execution Model
Instruction Level Parallelism
  Instruction on the single thread are pipelined to leverage Instruction Level Parallelism( ILP), in addition to the thread level parallelism
Other Notes

## Slide 43: CUDA Execution Model
Resources on a local context:
  Program Counters
  Registers
  Shared Memory
Other Notes
NOTE: If there is not enough resources for at least one block then the launch of the kernel will fail

## Slide 44: Profiling Tools

## Slide 45: Profiling Tools
Why do we use GPUs?
  Performance
How do we measure performance?
  We measure execution time.
  Use event handlers provided by CUDA.
Measuring Performance

## Slide 46: Profiling Tools
Specific data types:
Using the data types to measure time:
CUDA Events
//Time variables
cudaEvent_t start, stop;
float time;
cudaEventCreate(&start);
cudaEventCreate(&stop);
cudaEventRecord(start, 0);
// Put your code here…. (Kernel call)
cudaEventRecord(stop, 0);
cudaEventSynchronize(stop); // Wait for event to happen
// Display time
cudaEventElapsedTime(&time, start, stop);
printf("Parallel Job time: %.2f ms", time);
Second parameter associated to stream, usually stream 0

## Slide 47: Profiling Tools
CUDA Events
//create events
cudaEvent_t event1, event2;
cudaEventCreate(&event1);
cudaEventCreate(&event2);
//record events around kernel launch
cudaEventRecord(event1, 0); //where 0 is the default stream
kernel<<<grid,block>>>(...); //also using the default stream
cudaEventRecord(event2, 0);
//synchronize
cudaEventSynchronize(event1); //optional
cudaEventSynchronize(event2); //wait for the event to be executed!
//calculate time
float dt_ms;
cudaEventElapsedTime(&dt_ms, event1, event2);

## Slide 48: Profiling Tools
Now that we can measure performance, what if our code is taking too long?
How can we improve our code?
Best guideline
  Use profiling tools
Profiling Performance

## Slide 49: Profiling Tools
Command line profiler
  Compute time in each kernel
  Compute memory transfer time
  Collect metrics and events
  Support complex process hierarchy’s
  Collect profiles for NVIDIA Visual Profiler
  No need to recompile
NVPROF

## Slide 50: Profiling Tools
Compile binary with some information so nvprof / nvvp can track line numbers
NVPROF

## Slide 51: Profiling Tools
Instructions:
Collect profile information for the program by running
  nvprof ./exec
View available metrics
  nvprof --query-metrics
View global load/store efficiency
  nvprof -metrics gld_efficiency,gst_efficiency ./exec
Store a timeline to load in NVVP
  nvprof -o profile.timeline ./exec
Store analysis metrics to load in NVVP
  nvprof -o profile.metrics --analysis-metrics ./exec
NVPROF
Timeline of CUDA runtime calls, kernel execution times, etc.
Basically no run time overhead
Detailed performance data from each kernel execution. Large run time overhead

## Slide 52: Profiling Tools
NVVP

## Slide 53: Profiling Tools
Note: We will not use NVVP today (or tomorrow)
Instructions
Import nvprof profile into NVVP
  Launch nvvp
  Click file/ import/ nvprof/ next/ single process/ next /browse
    Select profile.timeline
  Add metrics to timeline
    Click on 2nd browse
    Select profile.metrics
  Click finish
Explore timeline
  Control + mouse drag in timeline to zoom in
  Control + mouse drag in measure bar (on top) to measure time
NVVP

## Slide 54: Takeaways
How to get close to peak performance?
Potential for floating point performance on GPUs is huge
  Integers less so
  Difficult to achieve!
Use memories efficiently:
  Avoid unnecessary data transfers
  Keep data being accessed often close to the processing elements
  Use registers and shared memory
Avoid control flow divergence
  Very few if statements

## Slide 55: Takeaways
Writing a CUDA kernel is becoming easier, but getting good performance is not.
Know the tools you have available
  Profiling is key to performance
Fitting your application to the GPU memory hierarchy is critical for performance
Resources are not infinite, optimization without thinking about the available resources could adversely affect performance.