## Slide 1: GPU Programming (in CUDA)
Julian Gutierrez
Fall 2018
Session 4

## Slide 2: Outline
Lab 1 summary
CUDA Memory Model
  Overview and Concepts
  Global Memory
  Registers
  Local Memory
  Shared Memory
  Caches
  Constant Memory and Texture Memory
Synchronization

## Slide 3: CUDA Memory Model

## Slide 4: CUDA Memory Model
Why do we need to understand the memory model?
  Memory accesses will affect performance drastically
  Memory patterns allow you to control these effects
  Maximize resource usage by taking care of the LD/ST units
  To do this, we use data locality

## Slide 5: CUDA Memory Model
Generally, applications don’t have random accesses
  Random accesses are very hard to improve
Having locality in our data helps improve the performance
There are two types of data locality that memory architectures make use of
Temporal locality
  Useful data tends to continue being useful
Spatial locality
  Useful data tends to be followed by more useful data
Notes: Explain how a cache works. Uses these two to keep program execution running.
Caches are a memory that is really close to the processor (fast, but small because its expensive).
They use temporal locality because stuff that the processor needs, it keeps it there because theres a high probability it will request it again
They use spatial locality because when a processor requests data, it brings that data and more (a block) because theres a possibility it will use that data too.

## Slide 6: CUDA Memory Model
Example
  CPU Caches
    They bring more than just the address being requested (block of memory)
    They remove the least recently used block from the cache when a new block comes in (eviction)
  GPUs exploit locality at different levels of the memory model
Notes: Explain how a cache works. Uses these two to keep program execution running.
Caches are a memory that is really close to the processor (fast, but small because its expensive).
They use temporal locality because stuff that the processor needs, it keeps it there because theres a high probability it will request it again
They use spatial locality because when a processor requests data, it brings that data and more (a block) because theres a possibility it will use that data too.

## Slide 7: CUDA Memory Model
Memories available on the GPU
  Registers
  Shared Memory
  Local Memory
  Constant Memory
  Texture Memory
  Global Memory

## Slide 8: CUDA Memory Model
Global Memory
  Resides in device memory
  Global scope: device level
  Largest memory on the GPU
  Highest latency (~100s of cycles)
  If it’s so slow, how can we use it efficiently?

## Slide 9: CUDA Memory Model
Global Memory
  Accesses are organized by half warps (16 threads)
  Accesses are done in 32, 64 and 128 byte segments
  Consecutive addresses are read quickly
  Certain non-sequential access patterns to global memory degrade performance
  Allocations are aligned to multiples of 256 bytes (or more) for performance purposes
  Accesses can be done in as little as one transactions for all the half warp, under certain conditions

## Slide 10: CUDA Memory Model
Global Memory
  This concept is called Memory Coalescing
  Find the segment containing the address request of the lowest numbered active thread
  Find all other active threads requesting in same segment
  Reduce transaction size (if possible)
  Mark the service threads as inactive
  Repeat until all threads in ½ warp
  are complete

## Slide 11: CUDA Memory Model
Example: 2D data
All warps in a block access consecutive elements within a row as they step through neighboring columns.
Accesses by threads in a block along a column don’t coalesce.

## Slide 12: CUDA Memory Model
In Summary
  GM has very high latency (~100 cycles per read)
  Resides in the RAM memory of the GPU
  We want half a warp to access addresses that fall into same 32, 64 or 128 byte blocks to coalesce the reads (convert multiple memory requests into a single one)
  Basically… We want very predictable and ordered accesses in memory. We will discuss this further in the hands-on lab.

## Slide 13: CUDA Memory Model
Registers
  The fastest memory
  Variables are automatically assigned to registers
  Some arrays might be declare as registers if the size is determined at compilation time and are fairly small

## Slide 14: CUDA Memory Model
Registers
  The fastest memory
  Variables are automatically assigned to registers
  Some arrays might be declare as registers if the size is determined at compilation time and are fairly small
__global__ void matrixMulKernel( float *devA, float *devB, float *devC, int row, int col, int k){
int txID = blockIdx.x * blockDim.x + threadIdx.x;
int tyID = blockIdx.y * blockDim.y + threadIdx.y;
if ((txID < col) && (tyID < row))
{
float Pvalue = 0;
for(int w=0; w<k; w++)
{
Pvalue += devA[tyID*k+w] * devB[w*k+txID];
}
devC[tyID*k+txID] = Pvalue;
}
}
Registers

## Slide 15: CUDA Memory Model
Registers
  Remember: Register File size is 64 K entries
  Registers are private for each thread.
  Kepler supports a maximum of 255 registers per thread.
  Example:
nvcc -Xptxas -v,-abi=no matrixMul.cu -o matrixMul
ptxas warning : 'option -abi=no' might get deprecated in future
ptxas info : 0 bytes gmem
ptxas info : Compiling entry function '_Z15matrixMulKernelPfS_S_iii' for 'sm_20'
ptxas info : Used 14 registers, 68 bytes cmem[0]
Note: Parallel Thread Execution (PTX) is a pseudo-assembly language used in Nvidia's CUDA programming environment

## Slide 16: CUDA Memory Model
Registers
  What happens if we exceed register hardware limit?
    Spills!
    It will significantly impact performance.
    It will spill to local memory.
Where is Local Memory?
In DEVICE MEMORY!

## Slide 17: CUDA Memory Model
Local Memory
  Variables that cannot fit on the registers space go to Local Memory
    Local array that indexes cannot be defined in compilation time
    Large local array that consumes too much register space
    Any variable that doesn’t fit in the register limit
  Remember, Local memory is actually stored in DEVICE MEMORY!
  The reads to Local Memory are as slow as Global Memory… kind of…
  In the Kepler Architecture, LM reads are cached in L1 cache, GM reads aren’t (by default)

## Slide 18: CUDA Memory Model
Shared Memory
  It is on-chip, therefore:
    It has a much higher bandwidth
    Lower latency
    Much smaller size
  It works at a block-level granularity
    Threads in a block can access the same shared memory space
    When a block is done, its shared memory will be released
    Use __syncthreads() to synchronize threads in the block to avoid hazards or race conditions

## Slide 19: CUDA Memory Model
Shared Memory
  It can be declared in the kernel (statically) or in the kernel call (dynamically).
  Use attribute: __shared__
__global__ void staticReverse(int *d, int n) {
__shared__ int s[64];
int t = threadIdx.x;
int tr = n-t-1;
s[t] = d[t];
__syncthreads();
d[t] = s[tr];
}
__global__ void dynamicReverse(int *d, int n) {
extern __shared__ int s[];
int t = threadIdx.x;
int tr = n-t-1;
s[t] = d[t];
__syncthreads();
d[t] = s[tr];
}

## Slide 20: CUDA Memory Model
Shared Memory
  It can be declared in the kernel (statically) or in the kernel call (dynamically).
  Use attribute: __shared__
…
// run version with static shared memory
cudaMemcpy(d_d, a, n*sizeof(int), cudaMemcpyHostToDevice);
staticReverse<<<1,n>>>(d_d, n);
cudaMemcpy(d, d_d, n*sizeof(int), cudaMemcpyDeviceToHost);
for (int i = 0; i < n; i++) if (d[i] != r[i])
printf("Error: d[%d]!=r[%d] (%d, %d)n", i, i, d[i], r[i]);
// run dynamic shared memory version
cudaMemcpy(d_d, a, n*sizeof(int), cudaMemcpyHostToDevice);
dynamicReverse<<<1,n,n*sizeof(int)>>>(d_d, n);
cudaMemcpy(d, d_d, n * sizeof(int), cudaMemcpyDeviceToHost);
for (int i = 0; i < n; i++) if (d[i] != r[i])
printf("Error: d[%d]!=r[%d] (%d, %d)n", i, i, d[i], r[i]);
..
What if you need multiple dynamically sized arrays in a single kernel?
You must declare a single extern unsized array as before, and use pointers into it to divide it into multiple arrays
Basically, don’t do it...
Just don’t…

## Slide 21: CUDA Memory Model
Shared Memory
  Another positive feature is that it is programmable on Kepler Architecture.
  You can assign the amount of memory you need.
    Shared memory and the L1 cache use the same physical space of 64K on-chip memory
cudaDeviceSetCacheConfig(cudaFuncCachePreferL1);
Options are:
cudaFuncCachePreferL1
cudaFuncCachePreferShared
cudaFuncCachePreferEqual

## Slide 22: CUDA Memory Model
Shared Memory
  This is usually the best way to optimize your algorithms memory behavior if there are multiple accesses to those memory addresses.
  Example:
__global__ void compute_it(float *data) {
  int tid = threadIdx.x;
  __shared__ float myblock[1024];
  float tmp;
  // load the thread's data element into shared memory
  myblock[tid] = data[tid];
  // ensure that all threads have loaded their values into
  // shared memory; otherwise, one thread might be computing
  // on uninitialized data.
  __syncthreads();
  // compute the average of this thread's left and right neighbors
  tmp = (myblock[tid>0?tid-1:1023] + myblock[tid<1023?tid+1:0]) * 0.5f);
  // square the previousr result and add my value, squared
  myblock[tid] = tmp*tmp + myblock[tid]*myblock[tid];
  // write the result back to global memory
  data[tid] = myblock[tid];
}

## Slide 23: CUDA Memory Model
Shared Memory
  So, why is Shared Memory so fast?
  Shared memory is divided into banks.

## Slide 24: CUDA Memory Model
Shared Memory
  Successive 32 bit words are assigned to successive banks
  For devices of compute capability 2.x or higher (fermi)
    Number of banks = 32
    Bandwidth is 32 bits per bank per 2 clock cycles
    Shared memory requests for a warp are not split
    Increased susceptibility to conflicts
    But no conflicts if access to bytes in same 32 bit word

## Slide 25: CUDA Memory Model
Shared Memory
  Access to shared memory is fast unless:
  2 or more threads in a warp access the same bank: we have a conflict
  If two or more addresses of a memory request are in the same bank, the accesses are serialized (Bank conflicts exist only within a warp)
  Exception: if all access the same address: broadcast

## Slide 26: CUDA Memory Model
Shared Memory
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R

## Slide 27: CUDA Memory Model
Shared Memory
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R

## Slide 28: CUDA Memory Model
Shared Memory
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R

## Slide 29: CUDA Memory Model
Shared Memory
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R

## Slide 30: CUDA Memory Model
In summary
  Very Fast (2 cycles per read)
  Divided into banks (32)
  We don’t want to access the same bank with threads in the same warp (bank conflicts, serialize the reads) unless they all access the same 32 bit address (we can broadcast the value to all the threads)
  Very useful if addresses are requested multiple times from global memory (reduce the reads from global memory).
  Requires extra manual work, and synchronization between threads in a block

## Slide 31: CUDA Memory Model
Caches
  Non-programmable memory
  Four types of caches:
    L1 cache
    L2 cache
    Read-only constant memory
    Read-only texture memory

## Slide 32: CUDA Memory Model
Caches
  One L1 per-SM
  One L2 for all SMs
  L1 and L2 store data for local and global memory (that includes register spills)
  GPUs like Kepler can configure that reads are cached in L1 and L2, or just L2 (default)
  Memory store operations cannot be cached

## Slide 33: CUDA Memory Model
Constant Memory
  Read-only and resides on device memory
  It has its own separate cache
  It has to be declared on a global scope outside of the kernel
  Limited resource: 64K for all compute capabilities
  Use attribute: __constant__

## Slide 34: CUDA Memory Model
Constant Memory
  Host has to initialize it:
  It performs better when all threads in a warp access the same memory address
  DON’T USE IT if all threads in a warp access different memory addresses and is only accessed once
  The variables in constant memory don’t have to be declared in the kernel invocation
cudaError_t cudaMemcpyToSymbol(const void* symbol, const void* src, size_t count);

## Slide 35: CUDA Memory Model
Constant Memory
  Performance Considerations
    Declaring memory as constant constrains the usage to read-only
    Reading from constant memory can conserve memory bandwidth when compared to reading the same data from global memory.
    There are 2 reasons why reading from 64 KB constant memory saves bandwidth:
      A single read from constant memory can be broadcasted to other threads, effectively saving up to 15 reads.
      Constant memory is cached, so consecutive read of the same address will not incur any additional memory traffic.

## Slide 36: CUDA Memory Model
Constant Memory
  Performance Considerations
    There can be a downgrade of the performance when using constant memory
    The half-warp broadcast feature can degrade the performance when all 16 threads read different addresses
    If all 16 threads in a half-warp need different data from constant memory, the 16 different reads get serialized

## Slide 37: CUDA Memory Model
Texture Memory
  It resides in device memory as well
  It is cached in a per-SM fashion
  It belongs to the scope of global memory but it is accessed through a dedicated read-only cache
  Recommended for use when data has 2D (3D) spatial locality (i.e. imaging)

## Slide 38: CUDA Memory Model
Texture Memory
  Example of how 2D spatial locality could work

## Slide 39: CUDA Memory Model
Texture Memory
  Example of how 2D spatial locality could work (Z-ORDER)
  Regular Memory Addresses
  Reordered Memory Addresses

## Slide 40: CUDA Memory Model
Texture Memory
  The easiest way to use texture memory, is by reference.

## Slide 41: CUDA Memory Model
Summary
  Each thread can:
  Read/write per-thread registers
  Read/write per-thread local memory
  Read/write per-block shared memory
  Read/write per-grid global memory
  Read/only per-grid constant memory

## Slide 42: CUDA Memory Model
Summary
  Type Qualifier table
  Notes:
    __device__ not required for __local__, __shared__, or __constant__
    Automatic variables without any qualifier reside in a register
      Except arrays that reside in local memory
      Or not enough registers available for automatic variables
Variable declaration | Memory | Scope | Lifetime
Int LocalVar; | Register | Thread | Thread
Int LocalArray[10]; | Local | Thread | Thread
[__device__] __shared__ int SharedVar; | Shared | Block | Block
__device__ int GlobalVar; | Global | Grid | Application
[__device__] __constant__ int ConstantVar; | Constant | Grid | Application

## Slide 43: CUDA Memory Model
Summary
  Type Qualifier table
  Notes:
    Scalar variables reside in on-chip registers (fast)
    Shared variables reside in on-chip memory (fast)
    Local arrays and global variables reside in off-chip memory (slow)
    Constants reside in cached off-chip memory
Variable declaration | Memory | Scope | Lifetime
Int LocalVar; | Register | Thread | Thread
Int LocalArray[10]; | Local | Thread | Thread
[__device__] __shared__ int SharedVar; | Shared | Block | Block
__device__ int GlobalVar; | Global | Grid | Application
[__device__] __constant__ int ConstantVar; | Constant | Grid | Application

## Slide 44: Synchronization
Many applications require different means of synchronization.
  Intra Block
  Inter Block
  CPU/GPU concurrent execution
How can we do these?

## Slide 45: Synchronization
Many applications require different means of synchronization.
  Intra Block
    __syncthreads()
      Must be reached by all threads from the block.
      Ensures that for all threads in the block, the code preceding the instruction is executed before the instructions following it.
    Atomic operations (in shared memory)

## Slide 46: Synchronization
Many applications require different means of synchronization.
  Inter Block
    No explicit way of doing this
      Terminate kernel at synchronization point, and then launch new kernel to continue after.
    Atomic operations (in global memory, should be avoided)
Notes: In fact, the concept of blocks in CUDA is that some may be launched only after some other blocks already ended its work, for example, if the GPU it is running on is too weak to process them all in parallel.
The best way that I can suggest, is to simply terminate your kernel at the synchronization point, and then launch a new kernel which would continue with your job.
Global barriers can be hacked together using atomic functions to implement a semaphore in device memory, but they tend to be dangerous because you have no guarantee that all of your blocks are running simultaneously, and blocks waiting at the barrier are not going to be preempted so the non-running blocks can make progress.
That will create a deadlock.

## Slide 47: Synchronization
Many applications require different means of synchronization.
  CPU/GPU concurrent execution
    Copy data back and forth

## Slide 48: Synchronization
Race Condition
  An undesirable situation that occurs when a device or system attempts to perform two or more operations at the same time, but because of the nature of the device or system, the operations must be done in the proper sequence to be done correctly.
How can we avoid this on a GPU?

## Slide 49: Synchronization
Atomic Instructions
  Atomic instructions are special hardware instructions that perform an operation on one or more memory locations atomically (indivisible or uninterruptible).
  An atomic operation either succeeds or fails in its entirety, regardless of what instructions are being executed by other threads.

## Slide 50: Synchronization
Use of atomic operations
  Collaboration
    Atomics on an array that will be the output of the kernel
      Histogram
  Synchronization
    Atomics on memory locations that are used for synchronization or coordination
      Counters, locks, flags…
CUDA provides atomic functions on shared memory and global memory

## Slide 51: Synchronization
Arithmetic functions
  Add, sub, max, min, exch, inc, dec, CAS
Bitwise functions
  And, or, xor
CUDA: int atomicAdd(int*, int);
PTX: atom.shared.add.u32 &r25, [%rd14],1;
SASS:
Lock/update/unlock vs native atomic

## Slide 52: Synchronization
Atomic conflict degree
  Intra-warp conflict degree from 1 to 32