## Slide 1: GPU Programming (in CUDA)
Julian Gutierrez
Spring 2019
Session 8

## Slide 2: Outline
Applications
  Parallel Reduction
  Prefix Sum (Scan)
  Histogram
  Convolution

## Slide 3: Parallel Reduction
A popular class of computation
Goal: To master the concept of control divergence through reduction trees (how to be work efficient).

## Slide 4: Parallel Reduction
Example
Calculate Max Value from vector:
A parallel reduction tree algorithm performs N-1 operations in log(N) steps

## Slide 5: Parallel Reduction
A commonly used strategy for processing large input data sets
  There is no required order of processing elements in a data set (associative and commutative)
  Partition the data set into smaller chunks
  Have each thread process a chunk
  Use a reduction tree to summarize the results from each chunk into the final answer
Google and Hadoop MapReduce frameworks are examples of this pattern
We will focus on the reduction tree step for now.

## Slide 6: Parallel Reduction
Example: Handling privatization
  Multiple threads write into an output location
  Replicate the output location so that each thread has a private output location
  Use a reduction tree to combine the values of private locations into the original output location

## Slide 7: Parallel Reduction
Use: Summarize a set of input values into one value using a “reduction operation”
  Max
  Min
  Sum
  Product
You need to initialize the result as an identity value for the reduction operation
  Smallest possible value for max reduction
  Largest possible value for min reduction
  0 for sum reduction
  1 for product reduction

## Slide 8: Parallel Reduction
For N input values, the reduction tree performs:
  (1/2)N + (1/4)N + (1/8)N + … (1/N) = N-1 operations
  In log(N) steps – 1 000 000 input values take 20 steps
    Assuming that we have enough execution resources
  Average parallelism (N-1)/log(N)
    For N = 1 000 000 average parallelism is 50 000
    However, peak resource requirement is 500 000!
This is a work-efficient parallel algorithm
  The amount of work done is comparable to sequential
  Many parallel algorithms are not work efficient

## Slide 9: Parallel Reduction
An example

## Slide 10: Parallel Reduction
An example
  Each thread block takes 2*BlockDim input elements
  Each threads loads 2 elements into shared memory
Notes: Example:
Block size = 4 (tid = 0-3)
Vector = 3 1 7 0 4 1 6 3

## Slide 11: Parallel Reduction
Why do we need syncthreads()?
Thread 0 in each thread block write the sum of the thread block in partialSum[0] into a vector indexed by the blockIdx.x
There can be a large number of such sums if the original vector is very large
  The host code may iterate and launch another kernel
If there are only a small number of sums, the host can simply transfer the data back and add them together
Notes: Partial sum is in shared memory?
Do example on the board

## Slide 12: Parallel Reduction

## Slide 13: Parallel Reduction

## Slide 14: Parallel Reduction
A better reduction?

## Slide 15: Parallel Reduction
There’s a problem
  Idle threads!
  Half of the threads are idle on first loop iteration!
  This is wasteful….

## Slide 16: Parallel Reduction
Halve the number of blocks, and replace single load:
With two loads and first add of the reduction:
Notes: A few techniques to improve even further the performance

## Slide 17: Parallel Reduction
Unrolling the last warp
  As reduction proceeds, # “active” threads decreases
    When s <= 32, we have only one warp left
  Instructions are SIMD synchronous within a warp
  That means when s <= 32:
    We don’t need to __syncthreads()
    We don’t need “if (tid < s)” because it doesn’t save any work
  Lets unroll the last 6 iterations of the inner loop

## Slide 18: Parallel Reduction
Note: This saves useless work in all warps, not just the last one!
Without unrolling, all warps execute every iteration of the for loop and if statement

## Slide 19: Parallel Reduction

## Slide 20: Parallel Reduction
Please note: this warp synchronized technique only works in older models. After Volta, this technique is no longer valid due to the change in GPU architecture.
More on this:
  https://devblogs.nvidia.com/cooperative-groups/
  https://devblogs.nvidia.com/inside-volta/

## Slide 21: Prefix Sum (Scan)
Definition
  Prefix sum, cumulative sum, inclusive scan, or simply scan of a sequence of numbers x0, x1, x2, ... Gives a second sequence of numbers y0, y1, y2, ..., the sums of prefixes (running totals) of the input sequence.
  Any binary operation (not just the addition operation).
Example
  If (+) is addition, then scan on the set:
    Returns the set:
Note: Exclusive scan: last input element is not included in the result

## Slide 22: Prefix Sum (Scan)
A Naïve inclusive parallel Scan
  Assign one thread to calculate each y element
  Have every thread add up all x elements needed for the y element
Note: Parallel programming is easy as long as you do not care about performance
Notes: Write the code?

## Slide 23: Prefix Sum (Scan)
Hillis Steele Scan: A slight better version compared to naïve version.
Iterate log(n) times: Threads stride to n: Add pairs of elements stride elements apart. Double stride at each iteration. (note must double buffer shared memory arrays)
This scan algorithm is not that work efficient
  Sequential scan algorithm does n-1 adds
  How many does this one do?
  What happens if the # of elements is 10^6?
Notes: N^2

## Slide 24: Prefix Sum (Scan)
Even better one: Blelloch Scan.
Reduces in log(n), downsweeps in log(n).
Total steps: 2 log(n)
This scan algorithm is work efficient

## Slide 25: Prefix Sum (Scan)
Even better one: Blelloch Scan.
Reduces in log(n), downsweeps in log(n).
Total steps: 2 log(n)
This scan algorithm is work efficient

## Slide 26: Prefix Sum (Scan)
Useful in implementation of several parallel algorithms:
  Radix sort
  Quicksort
  String comparison
  Lexical analysis
  Stream compaction
  Polynomial evaluation
  Solving recurrences
  Tree operations
  histograms
Examples
  Assigning camp slots
  Assigning farmer market space
  Allocating memory to parallel threads
  Allocating memory buffer for communication channels
More info: https://developer.nvidia.com/gpugems/GPUGems3/gpugems3_ch39.html

## Slide 27: Histogram
A histogram is a graphical representation of the distribution of numerical data.
Bar Graph
Serial Algorithm
For (i=0; I < BIN_COUNT; i++)
result[i]=0;
For (i=0; I < measurements.size(); i++)
result[computeBin(measurements[i])]++;

## Slide 28: Histogram
Naïve implementation:
Notes: Whats the problem here?

## Slide 29: Histogram
Naïve implementation:

## Slide 30: Histogram
Naïve implementation using atomic operations (Method 1):
  This will avoid RAW hazards.

## Slide 31: Histogram
Naïve implementation using atomic operations (Method 1):
  This will avoid RAW hazards.
Notes: Yo choose the highest amount
Whats the problem? Data dependent!
What happens if all the data falls into the same bin?

## Slide 32: Histogram
Redefining the method. Local histogram + reduction (Method 2)

## Slide 33: Histogram
Redefining the method. Local histogram + reduction (Method 2)

## Slide 34: Histogram
Redefining the method. Sort then reduce by key (Method 3)

## Slide 35: Histogram
Final thoughts on histogram:
  Using Atomic operations
  Using per-thread histograms, and then reduce
  Sort, then reduce by key
Question
  256 elements, 8 bins. How many atomic adds are needed?
    Naive atomic technique. (256 threads)
    Processing 16 elements per thread with local histogram, and then atomics.

## Slide 36: Convolution
Applications
  A popular array operation that is used in various forms in signal processing, digital recording, image processing, video processing, and computer vision.
  Convolution is often performed as a filter that transforms signals and pixels into more desirable values
    Some filters smooth out the signal values so that one can see the big-picture trend
    Others like Gaussian filters can be used to sharpen boundaries and edges of objects in images

## Slide 37: Convolution

## Slide 38: Convolution
An array operation where each output data element is a weighted sum of a collection of neighboring input elements
The weights used in the weighted sum calculation are defined by an input mask array, commonly referred to as the convolution kernel
  We will refer to these mask arrays as convolution masks to avoid confusion.
  The same convolution mask is typically used for all elements of the array.

## Slide 39: Convolution
1D Convolution example
  Commonly used for audio processing
    Mask size is usually an odd number of elements for symmetry

## Slide 40: Convolution
Example
  A causal discrete-time FIR filter of order N, each value of the output sequence is a weighted sum of the most recent input values:
  Where:
    X[n] is the input signal
    Y[n] is the output signal,
    N is the filter order, an Nth-order filter has (N+1) terms on the right-hand side
    Bi is the value of the impulse response at the ith instance for 0<= I <= N of an Nth-order filter. If the filter is a direct form FIR filter then bi is also a coefficient of the filter.

## Slide 41: Convolution
Calculation of output elements near the boundaries (beginning and end) of the input array need to deal with “ghost” elements
  Different policies (0, replicates of boundary values, etc.)

## Slide 42: Convolution
This kernel forces all elements outside the vector range to 0

## Slide 43: Convolution
2D convolution
2D convolution – ghost cells

## Slide 44: Convolution
Tiled Convolution for 1D
__shared__ double N_ds[BLOCK_SIZE + 2 * RADIUS];
int gindex = threadIdx.x + blockIdx.x * blockDim.x;
int lindex = threadIdx.x + RADIUS;

## Slide 45: Convolution
Loading the internals
// Read input elements into shared memory
N_ds[lindex] = in[gindex]

## Slide 46: Convolution
Loading the left halo
if (threadIdx.x < RADIUS) {
N_ds[lindex - RADIUS] = (gindex - RADIUS >= 0) ? in[gindex - RADIUS]: 0.0;
}

## Slide 47: Convolution
Loading the right halo
if (threadIdx.x < RADIUS) {
N_ds[lindex + BLOCK_SIZE] = (gindex+BLOCK_SIZE < vector_size) ? in[gindex + BLOCK_SIZE]: 0.0;
}

## Slide 48: Convolution

## Slide 49: Convolution
Example: Shared memory data reuse, with radius of 2.
A stencil/convolution operation has a lot of potential for data reuse.
Image processing algorithms can commonly use this resource as well.
The Sobel filter is an example of this algorithm we will cover in the image processing class.